D840R-How to set the virtual server？

Product line: ADSL        Question category: Function configurations

Q：What is the function of a virtual server?

A： When you create a server such as a Web server, FTP server or game server in your router’s LAN side, you can let Internet users access the created server through the router’s WAN IP address by configuring virtual server.

The topology is as below:

I. Run a server on your computer

Take FTP Server for example. Click start(run and type cmd in the blank. In the new window, please type netstat -an. Then you can check whether the FTP server has been run successfully.

II. Physical connection:

III. Login to the management page of the router:

1. Open a web browser (IE, Firefox, Safari, etc.) and find the address bar, leaving it blank before typing in 192.168.1.1, and then press enter.

(Care: The address bar is in the most top of the web page after opening web browser).

2. Input the default username and password:admin in the following page, then click ok.

3. Please click on Advanced Settings->NAT->Virtual servers to display the page as below. Click Add.

4. You will see the page below. You can select a service and then ports will come out automatically, and then input a server IP address and click the first Save/Apply.

5. You can also set a service name and add a server by yourself in Customer Server. Then input an IP address for the server and input the ports and choose protocols. Click the second Save/Apply at last.

After the configurations above, client in the Internet can access the Server in your local network. For example, according to the topology, computer with IP address 2.2.2.2 in the Internet can access the FTP Server by ftp://1.1.1.1:21.