How to set the DHCP Server to assign a special IP address to a computer for the wireless router(R)

Product line: wireless     question category: function config

Q：Why we need set the static IP binding?

A：Sometimes we will want to assign a special IP address to special computers, you can achieve this by set static IP binding.

The Steps are as below:

1. Login to the home page of the router

2.Click DHCP Server(DHCP Client List on the left side of the homepage. Then please add the MAC address to the list and click Apply, then the computer with the MAC address will get the same IP address all the time.

For example, we want the computer with MAC address C8:3a:35:08:01:a1 get the IP address 192.168.80.120, you can set the router following the picture as below.