D820B-How to setup this modem?

Product line: ADSL             Question category: Internet settings

I. Physical connection:

- Telephone line to line port on D820B. PC to LAN port on D820B.

- Power on D820B.

- Change the IP of your pc into 192.168.1.x(x can anyone of 2 to 254)

- Type 192.168.1.1 into address bar on Web browser

- User name and password are both admin.

- Go to WAN Setup->ATM PVCs. Input VPI/VCI which got from your Internet service provider and then hit apply and save.

- If you see the following information. That’s mean it changed succefully.

- After you done all the steps, please change the IP of your computer into DHCP.