3G186R-How to control others connect to 3G186R by MAC filter?

Product line: 3G          Question category: Function configurations

Setup steps as follow:

1. Login To manage page of 3G186R and go to advanced

2. Advanced Settings(Firewall(MAC Filter. Enable

MAC Filter and choose Filter Mode.

3. Add pc MAC address and click ok to effect deny or allow to Internet.