3G611R (3G611R+)-How to manage the router remotely (Remote Web Management) ？

Product line: 3G          Question category: Function configurations

Q：Why we need to configure the Remote Management?

A：Sometimes, we need to manage router remotely in the office, you can achieve the function by the Remote WEB Management settings.

The topology is as below

The steps are as followings:

- Login the management page of the router.

- Click Security settings(Remote Web Management,

Tick Enable to force the Remote Web Management into effect.

For example, if you want to manage the router remotely by the devices with IP Address 202.96.134.33-202.96.135.205, then you can configure the router as below.

(1).Tick Enable to start the Remote Web Management.

(2).Input the management port number.

(3).Fill in the WAN IP Address segment which can manage the router remotely.

(4).Remember to click Apply to save the settings.

After the settings, if your IP address is during the segment 202.96.134.33-202.96.134.205, then you can manage your router remotely. Just type the http://the router’s WAN IP Address: 8080 in the address bar, then you can login to the management page of the router and management it remotely.

Note:

1. Type a specific Public IP address for the Remote Web Management IP Address means that you can only connect to this device remotely from a computer which is using this specific IP address.

2. We suggest you to change the default login Username and Password if you enabled the Remote Management feature, especially when you typed 0.0.0.0 as the Remote Web Management IP address.