A3-How to login to the homepage?

Product line: Wireless           Question category: Internet settings

The Connection Topology is as below:

The steps are as below:

1. Connect your computer to the LAN port with Ethernet cable and make sure that the power is supplied.

Note: The A3 is a wireless access point; it can’t provide the IP address for your computer.

You should set an IP address for your computer manually before login to the A3 web page. The default IP address of A3 is 192.168.0.254, so the IP address of your computer should be 192.168.0.XXX (1<=XXX<=253).

Then login to the home page of Wireless Router through type http://192.168.0.254 in the address bar in web browser (IE, Firefox, etc)

2. After login successfully, the following page will appear. Please click on Advanced Settings to finish the configurations.