A3-How to setup the AP mode?

Product line: Wireless     Question category: Function configurations

Q: When do we need to configure AP mode?

A：Sometimes we have one wired router, and we want to access the Internet wirelessly on laptop, the AP mode of A3 can help you to achieve it.

The connection topology as follows

The Steps are as below:

- First we should login to the homepage of A3. So please connect your computer to the A3 directly with an Ethernet cable, and then set an IP address (e.g. 192.168.0.10) for your computer, then login to the home page of A3 through type http://192.168.0.254 in the address bar.

- After login successfully, the following page will appear. Please click on Advanced Settings.

- In the homepage of A3, please click Wireless Settings, then click Wireless Basic Settings to choose AP mode and set the name of your wireless network, please change the SSID to tenda123 (SSID is the name of wireless network, you can name it by yourself) and choose channel 11 as the Channel, then click OK to save the settings.

- Click Wireless Settings(Wireless Security to set the password. Please choose WPA-PSK as Security Mode and AES as WPA Algorithms. In the box of the Key, please type your password which should be at least eight characters, then click OK to save.

- After configuration, connect A3 to your uplink router with a cable

- Please find the name of your wireless network and connect to it. It will ask you for a password, please type password and click Ok to connect.