How to setup the router for ADSL-Dial up(PPPoE) internet  connection mode?

Product line: Wireless   Question category: Internet settings

Step1 Connect the devices

Step2 Configure your computer

Step3 Setup the router

Step4 Check whether you can access internet

Connect the modem to the blue port of the router, then connect the router to your computer by a cable as the following picture.

Attention: After connection. the SYS light should be blinking, WLAN light should be on or blinking, one of LAN ports (12,3,4) is on, WAN light should be on or blinking

1.Open Network and Sharing Center.

2. Click on Change adapter settings

3.Right click on Local Area Connection, then choose Properties.

4.Double click on Internet Protocol Version 4.

5.Choose Obtain an IP address automatically and Obtain DNS Server address automatically, then click OK, the previous page click OK.

1.Open a browser or safari, then input 192.168.0.1 in the address bar, click Enter.

2. Choose ADSL-dial up, input the information, set a wireless password, click OK, then click Advanced Settings.

If you can’t login to this page, please click this link

If the connection status shows Connected, it means that you can have internet.Please check.

If you can’t access internet, click this link.

Wireless settings, please click this link